## Slide 1: ENGI 301 Air Quality Data Module PCB Proposal
16 October 2021
Samuel Xu

## Slide 2: Background Information
What is being proposed?
  Pictures of prototype
  Links to your Hackster page / GitHub
What changes (if any) are you going to make based on your prototype?

## Slide 3: Background Information
  Proposal of an air quality data collection and display system that includes:
    PMx.x (generally 2.5 or 10 is used), humidity (%), temperature (both C and F), CO2 (PPM) and TVOC (PPB).
  Planned Improvements
    Run on startup
    PCB adaptation
    Creation of 3D printable / laser cut case
    Exploring alternate or new sensors (ie: PMSA003I, which uses I2C instead of serial) to fix dust particle reading issues

## Slide 4: System Block Diagram
PocketBeagle
Contains:
OSD3358
I2C1
Humidity & Temp (AHT10)
2.2” LCD Display
CO2 & TVOC Sensor (CCS811)
Computer / 5V USB Power Supply
USB0
UART0
Dust Sensor (PMS5003)
TX/RX
SPI0

## Slide 5: Mechanical Drawing
4”
3.5”
CCS811 (3/4” x 5/8”)
2”
2.2” LCD Display (3 ½” x 2 7/16”)
Pocket Beagle
2 1/8” x 1 3/8”
FRONT
MIDDLE
USB
AHT10 (3/8” x 9/16”)
PMS5003
1 15/16” x 13/16”
5V Power Supply (Optional)

## Slide 6: Mechanical Drawing Pt. 2
4”
3.5”
BACK
PMS5003 / PMSA0031
1 15/16” x 13/16”
5V Power Supply (Optional)
The Mechanical Drawing is spread out over three stacked layers for more efficient packaging
  The power supply and air quality sensor are much thicker in the unspecified dimension than the PocketBeagle.
  A PCB may not be sufficient for every connection, some wires may need to be integrated.

## Slide 7: Components Required
All the components required consist of:
  PocketBeagle (already have)
  CCS811 CO2 and TVOC sensor(already have)
  AHT10 temperature and humidity sensor (already have)
  ILI9341 LCD screen (already have)
  PMS5003 Dust Sensor (already have)
  PMSA0031 Dust Densor (try to replace)
  PCB (to be designed and commissioned)
  Wires / through hole pins / resistors (assuming not integrated to PCB) to join components
  5V USB power supply (optional and mechanical drawing subject to change depending on sizes available